## Slide 1: SMART INDIA HACKATHON 2026
TITLE PAGE
SIH26085
Problem Statement
Urban Flood Nowcasting System (Drainage and Rainfall Coupling)
Theme
Disaster Management
PS Category
Software
Team ID
[ENTER REGISTERED TEAM ID]
Team Name
[ENTER REGISTERED TEAM NAME]
From “How much rain?” → “Where will water accumulate?”

## Slide 2: IDEA TITLE
TEAM NAME
URBAN FLOOD NOWCASTING SYSTEM • Drainage + Rainfall Coupling
A coupled rainfall + drainage model forecasts street-level flooding before it becomes visible.
1 RAINFALL INPUT
IMD nowcast or historical replay Common grid for simulation
↓
2 URBAN RESPONSE
DEM + imperviousness Rain → runoff → surface flow
↓
3 DRAINAGE COUPLING
Drainage graph + hydraulic capacity Surcharge / backflow detection
↓
4 ACTIONABLE OUTPUT
0–180 min flood-depth ranges Risk streets + flood-safe routes
↓
CURRENT GAP
OUR MECHANISM
OPERATIONAL OUTCOME
Rainfall alone does not locate flooding
Couple runoff + terrain + drainage capacity/surcharge
See which streets flood, how deep, and when
USP • Predict the behaviour of the city’s water system — not just the rain forecast.

## Slide 3: TECHNICAL APPROACH
TEAM NAME
Rainfall input → runoff → surface flow → drainage hydraulics → flood depth → decision support
RAINFALL IMD / REPLAY
›
RUNOFF SCS-CN / Rational
›
SURFACE FLOW DEM + CA
›
DRAINAGE PySWMM / GNN
›
FLOOD DEPTH Surface + drainage
›
GIS + ROUTING MapLibre + A*
DATA LAYER
DEM / terrain
Land cover / imperviousness
Drainage graph / capacity
Historical flood labels
MVP MODEL
Physics-first: runoff + surface routing + simplified drainage hydraulics. No black-box flood claim.
FAST INFERENCE
GNN surrogate is an acceleration path for repeated drainage scenarios; validate against SWMM-generated references.
OUTPUT
Depth bands: 0–10 cm / 10–30 cm / 30–50 cm / >50 cm + road risk.
ESSENTIAL STACK
Python + FastAPI
React + MapLibre GL
PostgreSQL + PostGIS
GeoPandas + Rasterio
PySWMM + NetworkX
PyTorch Geometric

## Slide 4: FEASIBILITY AND VIABILITY
TEAM NAME
The MVP is intentionally bounded: one ward, explicit fallbacks, honest validation limits.
DATA FEASIBILITY
Public DEM + land-cover sources; OSM/OpenCity where available. Use historical replay when a live feed is unavailable.
MODEL FEASIBILITY
Single-ward MVP keeps the coupled model tractable: SCS-CN + cellular automata + simplified PySWMM.
DEPLOYMENT FEASIBILITY
Web GIS dashboard + API. No hardware dependency for the core software prototype.
KEY RISK
WHY IT MATTERS
MITIGATION
DEMO TRUTH
Drainage data gaps
Real topology/capacity may be unavailable
Use OpenCity/municipal GIS when possible; otherwise label approximation
Synthetic ≠ municipal
No live rainfall feed
Nowcasting cannot depend on an unavailable API
Historical replay is the deterministic fallback
Demo mode is explicit
Validation scarcity
Depth claims need ground truth
Use NRSC/historical event overlays + error metrics when labels exist
Targets ≠ achieved
COST PRINCIPLE • Open-source core + public data + modest cloud/local inference
SCALE PATH • Ward → City → State → multi-city

## Slide 5: IMPACT AND BENEFITS
TEAM NAME
The value is not another map — it is earlier, safer and more targeted decisions.
BEFORE
AFTER
Rainfall known
→
Flood locations forecast
Manual / reactive checks
→
Automated risk prioritization
Static road status
→
Flood-aware routing
City-wide warning
→
Street / segment-level action
WHO BENEFITS
• Municipal flood managers • Emergency services • Traffic & public transport • Citizens & businesses • Urban planners
WHAT WE MEASURE
• Warning lead time • Flood-depth MAE / RMSE • Inundation IoU / F1 • Affected-road coverage • Route risk / detour
CORE OUTCOME → Forecast water accumulation early enough to pre-position resources, reroute traffic, and warn people.
All performance numbers are targets until validated on event-level data.

## Slide 6: RESEARCH AND REFERENCES
TEAM NAME
SIH26085 | Ministry of Earth Sciences | Disaster Management | Software | Urban Flood Nowcasting System (Drainage and Rainfall Coupling)
PROBLEM / DATA EVIDENCE
METHOD / PRIOR ART
SIH 2026 problem listing
https://sih2026.vuce.in/ps/SIH26085
Google Flood Hub – model scope & urban flash flood beta
support.google.com/flood-hub
ISRO / CWC River Basin Atlas & water-resource datasets
isro.gov.in / indiawris.gov.in
USGS SRTM / global DEM data
earthexplorer.usgs.gov
OpenCity Chennai – stormwater drainage maps
opencity.in
EPA SWMM – drainage hydraulics
github.com/USEPA/Stormwater-Management-Model
PySWMM – Python SWMM interface
github.com/pyswmm/pyswmm
HybridUrb – hybrid urban flood modelling
github.com/xldeltares/hybridurb
FloodGNN-GRU – spatio-temporal flood prediction
2024 research literature
GNN surrogate modelling – urban drainage hydraulics
2024 Water Research literature
Research basis from supplied project analysis: SCS Curve Number • Rational Method • Manning • SWMM • GNN drainage surrogates • cellular-automata surface routing.
References/URLs are provided for verification; the deck does not claim unvalidated model accuracy.