## Slide 1: SMART INDIA HACKATHON 2026
TITLE PAGE
SIH26085
Problem Statement
Urban Flood Nowcasting System (Drainage and Rainfall Coupling)
Theme
Disaster Management
PS Category
Software
Team ID
[ENTER REGISTERED TEAM ID]
Team Name
[ENTER REGISTERED TEAM NAME]
From “How much rain?” → “Where will water accumulate?”

## Slide 2: IDEA TITLE
TEAM NAME
URBAN FLOOD NOWCASTING SYSTEM • Drainage + Rainfall Coupling
A coupled rainfall + drainage model forecasts street-level flooding before it becomes visible.
1 RAINFALL INPUT
IMD nowcast or historical replay Common grid for simulation
↓
2 URBAN RESPONSE
DEM + imperviousness Rain → runoff → surface flow
↓
3 DRAINAGE COUPLING
Drainage graph + hydraulic capacity Surcharge / backflow detection
↓
4 ACTIONABLE OUTPUT
0–180 min flood-depth ranges Risk streets + flood-safe routes
↓
CURRENT GAP
OUR MECHANISM
OPERATIONAL OUTCOME
Rainfall alone does not locate flooding
Couple runoff + terrain + drainage capacity/surcharge
See which streets flood, how deep, and when
USP • Predict the behaviour of the city’s water system — not just the rain forecast.

## Slide 3: TECHNICAL APPROACH
TEAM NAME
Rainfall → Runoff → Surface Flow → Drainage → Flood Depth → Decision Support
RAINFALL
IMD / Replay
→
RUNOFF
SCS-CN / Rational
→
SURFACE FLOW
DEM + CA
→
DRAINAGE
PySWMM / GNN
→
FLOOD DEPTH
Surface + Drainage
→
GIS + ROUTING
MapLibre + A*
DATA LAYER
DEM / terrain
Land cover / imperviousness
Drainage graph / capacity
Historical flood labels
MVP MODEL
Physics-first — no black-box claims
FAST INFERENCE
GNN surrogate, validated vs. SWMM
OUTPUT
4 depth bands + road risk
ESSENTIAL
STACK
Python + FastAPI
React + MapLibre GL
PostgreSQL + PostGIS
GeoPandas + Rasterio
PySWMM + NetworkX
PyTorch Geometric

## Slide 4: FEASIBILITY AND VIABILITY
TEAM NAME
Bounded MVP — one ward, explicit fallbacks, honest validation limits.
DATA FEASIBILITY
Public DEM + land cover; historical replay fallback
MODEL FEASIBILITY
Single-ward scope keeps the model tractable
DEPLOYMENT FEASIBILITY
Web GIS dashboard + API — no hardware needed
KEY RISKS
Drainage data gaps
Approximate when municipal data is missing
Synthetic ≠ municipal
No live rainfall feed
Historical replay is the deterministic fallback
Demo mode is explicit
Validation scarcity
Validate vs. NRSC / historical overlays when available
Targets ≠ achieved
COST PRINCIPLE
Open-source core + public data + modest inference
SCALE PATH
Ward → City → State → multi-city

## Slide 5: IMPACT AND BENEFITS
TEAM NAME
Not another map — earlier, safer, more targeted decisions.
BEFORE
AFTER
Rainfall known
→
Flood locations forecast
Manual / reactive checks
→
Automated risk prioritization
Static road status
→
Flood-aware routing
City-wide warning
→
Street / segment-level action
WHO BENEFITS
• Flood managers
• Emergency services
• Traffic / transit
• Citizens
• Urban planners
WHAT WE MEASURE
• Warning lead time
• Depth accuracy
• Inundation match
• Road coverage
• Route risk
SMARTER
FASTER
SAFER
STRONGER
COMMUNITIES
All figures are targets until validated on event-level data.

## Slide 6: RESEARCH AND REFERENCES
TEAM NAME
SIH26085 | Ministry of Earth Sciences | Disaster Management | Software | Urban Flood Nowcasting System (Drainage and Rainfall Coupling)
PROBLEM / DATA EVIDENCE
METHOD / PRIOR ART
SIH 2026 problem listing
https://sih2026.vuce.in/ps/SIH26085
Google Flood Hub – model scope & urban flash flood beta
support.google.com/flood-hub
ISRO / CWC River Basin Atlas & water-resource datasets
isro.gov.in / indiawris.gov.in
USGS SRTM / global DEM data
earthexplorer.usgs.gov
OpenCity Chennai – stormwater drainage maps
opencity.in
EPA SWMM – drainage hydraulics
github.com/USEPA/Stormwater-Management-Model
PySWMM – Python SWMM interface
github.com/pyswmm/pyswmm
HybridUrb – hybrid urban flood modelling
github.com/xldeltares/hybridurb
FloodGNN-GRU – spatio-temporal flood prediction
2024 research literature
GNN surrogate modelling – urban drainage hydraulics
2024 Water Research literature
Research basis from supplied project analysis: SCS Curve Number • Rational Method • Manning • SWMM • GNN drainage surrogates • cellular-automata surface routing.
References/URLs are provided for verification; the deck does not claim unvalidated model accuracy.